## Slide 1: Introduction of Code Coverage (Using VCS)
Jerry Chang
2020/02/13

## Slide 2: Outline
Code Coverage for VCS
  Coverage Types
  VCS Flow
  VCS Flow in csim_ASIC

## Slide 3: Outline
Code Coverage for VCS
  Coverage Types
  VCS Flow
  VCS Flow in csim_ASIC

## Slide 4: Coverage Type
According to the VCS coverage UG, it gives 5 kinds of coverage type
  Line Coverage
  Toggle Coverage
  Condition Coverage
  Branch Coverage
  FSM Coverage
Example A
Example B

## Slide 5: Example A

## Slide 6: Line Coverage
Which line has been executed in always block
  Green Executed
  Red Not executed
Line Coverage Rate (Statement) : 5/7 = 71.43%
Line Coverage Rate (Block) : 4/5 = 80.0%

## Slide 7: Toggle Coverage
Signal/Port (i.e., reg/wire/input/output …) transition
  Transitions, 01, 10
Toggle Coverage Rate: 65/152 = 42.76%

## Slide 8: Condition Coverage
Condition in sub expression or expression are evaluated (0 and 1 are all evaluated).
Condition Coverage Rate: 1/5 = 20%

## Slide 9: Branch Coverage
Coverage of expression and case statements (e.g., if..else/case/‘?’) that affect the control flow
Branch Coverage Rate = 1/3 = 33.3%

## Slide 10: Coverage Type
According to the VCS coverage UG, it gives 5 kinds of coverage type
  Line Coverage
  Toggle Coverage
  Condition Coverage
  Branch Coverage
  FSM Coverage
Example A
Example B

## Slide 11: Example B
State Bit : 2, 4 states
Transition Paths : c24 = 12

## Slide 12: FSM Coverage
FSM Coverage Rate = 6/12 = 50%
State: 2^2 = 4
Transition Paths : c42 = 12

## Slide 13: Outline
Code Coverage for VCS
  Coverage Types
  VCS Flow
    Compilation (vcs) & Simulation (simv)
    Converge Data Merge (urg)
    Debugging (dve or browser)
  VCS Flow in csim_ASIC

## Slide 14: VCS Flow
Compilation & Simulation
–lca (limited custom available) => 啟動license的命令語句
–cm line+fsm+cond+branch+tgl+assert =>打開不同種類的coverage分析
–cm_dir “coverage_dir” =>存取coverage data的資料夾路徑
–cm_hier “coverage_hierachy” =>需要分析coverage的hierarchy
    Converge Data Merge (urg)
–dir => 需要merge的所有coverage 資料夾
–metric line+fsm+cond+branch+tgl => 指定輸出的coverage類型
–report => 指定輸出coverage report的路徑
–format => 指定輸出report的格式(html、text)
    Debugging (dve or browser)

## Slide 15: VCS Flow in csim_ASIC
make pattern_name run_options COV=ON
make vcs_cov_merge
make vcs_cov_rpt