## Slide 1: Y10 2D command & Corresponding Reg. setting in DISP
Jerry Chang

## Slide 2: Abbreviation
Multi-Format Decoder (MFD)
DISP (DISPlay)
  Video Post Processor (VPP)
    Deinterlace Data FetCH (DDFCH)
    DEINTerlacing (DEINT)
  Auto Frame Rate Conversion (AFRC)

## Slide 3: Discussed Issues
MBus R/W sequences for DISPLAY
  Command formats in DISPs.
  R/W sequences using register controlling .
Memory mapping for DISP functions in DDR.

## Slide 4: Outline
Introduction
  2D Command
  Masters in DISP
MBUS Commands in DISP
  1/2D CMDs modification for 10-bit rawdata
Register Setting in DISP DDFCH using 2D CMDs
  Register Setting
  Example: Register setting by 2D commands
  Example: Read Sequence of Luma 720x576

## Slide 5: Intro. – MBUS 2D Command
where XADDR, YADDR are defined in 2D command.
Every D(XADDR, YADDR ) represents a 4-byte data.
D(XADDR, YADDR)

## Slide 6: Intro. – MBUS 2D Command
Command Phase | Bits | Description
CMD | [2:0] | Command write: 3'b001 read: 3'b010
ADDR | [31:0] | Address 2D MODE: [22:12] y_addr [11:2] x_addr
BURST_LEN | [5:0] | Burst Length (Burst Unit: 64 bits, bus width)
BURST_SEQ | [2:0] | Burst Type 1D: 3'b000 2D: 3'b111 Others follow OCP Spec.
REQ_INFO | [1:0] | Command Type [0] : for urgent at ND1.0 and ND1.1
ADDR_SPACE | [10:0] | Address Space ( For 2D command ) [10:9]: PIC_INDEX (No used) [8:2] : BASE_INDEX : 0~127, #Reference frame [1:0] : 2D MODE 2'b00 : Linear mode 2'b01 : Frame mode 2'b10 : Field mode Others: Reserved *10'b1100 in some case is for MSI Command
BLOCK_HEIGHT | [5:0] | Block Height (Burst Unit: bytes)

## Slide 7: Intro. – Masters in DISP

## Slide 8: MBus Commands in DISP
# | Master Name | CMD | BURST_SEQ | ADDR |  | REQ_INFO | BURST_ LENGTH | ADDR_SPACE |  |  | BLOCK_HEIGHT
 |  |  |  | BASE ADDRESS | INCR. OFFSET |  |  | PIC_INDEX | BASE_INDEX | 2D_MODE | 
10 | G2D | READ | 1D | Register Setting | 32(Minimum) | URGENT | 16/32 | 0s |  |  | 0
11 | VPP (DDFCH) | R/W | 1D | Register Setting | 128 (Minimum) | URGENT | 16/32 | 0s |  |  | 0
 |  | READ | 2D | Register Setting |  | URGENT | 16/32 | 2'b0 | Register setting | 2'b01 (Frame mode) | 1
16 | OSD | READ | 1D | Register Setting | 32(Minimum) | URGENT | 16/32 | 0s |  |  | 0
17 | AFRC | R/W | 1D | Register Setting | 128 (Minimum) | URGENT | 32 | 0s |  |  | 0
Only MFD and DISP in MBUS use 2D command.
G2D/OSD : 8bit YUV/RGB : 1D command
Source are not related with MFD.
VPP : MOTION/EDGE : 1D command, 8 bytes per 6 pixels.
For DEINT, not related with MFD.
8 bit LUMA/CHROMA: 1/2D CMD.
2D CMD is for MFD. Need to extend the bit width to 10 bits.
AFRC : 8bit YCbCr422: 1D command (TBD)
*This table are produced by my RTL code tracing.
It may have some differences in real case.

## Slide 9: 2D CMDs for 10-bit rawdata
# | Master Name | CMD | BURST_SEQ | ADDR | REQ_INFO | BURST_ LENGTH | ADDR_SPACE |  |  | BLOCK_HEIGHT
 |  |  |  |  |  |  | PIC_INDEX | BASE_INDEX | 2D_MODE | 
11 | VPP (DDFCH) | READ | 2D | Register Setting STARTPOINT + OFFSET [22:12] YADDR [11:2] XADDR | URGENT | 16/32 | 2'b0 | Register setting | 2'b01 (Frame mode) | 1
(XADDR , YADDR) = (XSTARTPOINT , YSTARTPOINT ) + (XOFFSET , YOFFSET )
(XSTARTPOINT, YSTARTPOINT)  Defined in registers G80.4, G80.5
One Transfer  MBus Data width = 8 bytes  ADDR = ADDR + 8  XADDR += 2
CASE: 8-bit extension CASE: 10-bit extension
WHEN BURST_LENGTH = 16
XOFFSET = 16*2 = 32  XOFFSET = 16*2*1.25 = 40
BURST_LENGTH = 16  BURST_LENGTH = 16 *1.25 = 20
WHEN BURST_LENGTH = 32
XOFFSET = 32*2 = 64  XOFFSET = 32*2*1.25 = 80
BURST_LENGTH = 32  BURST_LENGTH = 32 *1.25 = 40
YOFFSET = 1, no need to change.
All follows the rules of 8-byte alignment.

## Slide 10: 1D CMDs for 10-bit rawdata
# | Master Name | CMD | BURST_SEQ | ADDR |  | REQ_INFO | BURST_ LENGTH | ADDR_SPACE |  |  | BLOCK_HEIGHT
 |  |  |  | BASE ADDRESS | INCR. OFFSET |  |  | PIC_INDEX | BASE_INDEX | 2D_MODE | 
17 | AFRC | R/W | 1D | Register Setting | 128 (Minimum) | URGENT | 32 | 0s |  |  | 0
CASE: 10-bit extension
NEW BURST_LENGTH = 32*1.25 = 40
NEW INCR. OFFSET = 128*1.25 = 160

## Slide 11: MBus Read Sequence for MFD rawdata using 2D CMD
Register Setting
Read Sequence

## Slide 12: Register Setting for DDFCH
We have to clarity the following settings:
DISP
  2D CMD Enable – G80.28.6
  Setting for XSTARTPOINT, YSTARTPOINT – G80.0 and G80.1
  Frame Width and Height – G80.2 and G80.3
  Pointer to Reference Frame in SDCTRL – G80.17 to G80.22
    Pervious/Current/Next frame with Luma/Chroma
SDCTRL
  Address Mapping in SDCTRL – G36.0 to G39.31
  MB size setting matched with MFD

## Slide 13: 2D CMD Enable
Default : G80.28.6 = 1  Set to 2D mode
USER MODE

## Slide 14: Pointer to Reference Frame in SDCTRL
Current Frame
Next
Pervious
Pervious and next frames are used for DEINT.
This setting value will point to a corresponding address which stored in G36 to G39.

## Slide 15: Pointer to Reference Frame in SDCTRL
Example
Command Phase | Bits | Description
ADDR_SPACE | [10:0] | Address Space ( For 2D command ) [10:9]: PIC_INDEX (No used) [8:2] : BASE_INDEX : 0~127, #Reference frame [1:0] : 2D MODE 2'b00 : Linear mode 2'b01 : Frame mode 2'b10 : Field mode Others: Reserved *10'b1100 in some case is for MSI Command
e.g. Set G80.17 = 15’d35
35 % 32 = 1 … 3  G(36+1).(3-1)= G37.2
Appended in this filed for 2D CMDs.
SDCTRL can use this to identify the base address of data

## Slide 16: Actual Address mapping in SDCTRL
G36 to G39, total 128 registers
Actual MBUS ADDR:
0xb0000000 +
(BG_2D_BASE_INDEX * 1024)

## Slide 17: Actual Address mapping in SDCTRL
MFD and DISP must have the same value.
Write Frame Width = XX_XX_SIZE_X *16.
2’b00
2’b01
2’b10
(for DISP)
2’b11
(for MFD)

## Slide 18: Case: An example uses 2D commands
720x576 YUV420, MFD output using 2D CMDs
MFD follows the same setting with DISP
  Luma 720x576, stored in 0xa3086c00
  Chroma 720x288, stored in 0xa18de000

## Slide 19: Case : An Example with register setting for 2D CMDs

## Slide 20: Read Sequence of Luma 720x576
 | XADDR |  | 
YADDR | 0x00 | 0x40 | 0x80
0x00 | 0 | 3 | 4
0x01 | 1 | 2 | 5
0x02 | 6 | 8 | 10
0x03 | 7 | 9 | 11
0x04 | 12 | 15 | 16
0x05 | 13 | 14 | 17
… |  |  | 
0x23F (575) |  |  | 
Read Order
256x1 bytes data with BURST_WIDTH=32

## Slide 21
HISTORY, no patterns use 2D Commands